## Slide 1: K-12 Microelectronic Workshop Arduino Programming
1 struct instructor {
2 String name = “Yi Liu”;
3 String department = “Mechanical Engineering”;
4 String university = “University of Vermont”;
5 }

## Slide 2: Contents
2. First Arduino Program
  2.1 Arduino sketch structure
  2.2 Uploading
  2.3 Using delay — a blinking LED
  2.4 Debugging with Serial
  2.5 Summary

## Slide 3: 2.1 First Arduino program
1 void setup() {
2 // put your setup code here, to run once:
3 }
4
5 void loop() {
6 // put your main code here, to run repeatedly:
7 }
0_BasicStructure.ino

## Slide 4: 2.1 First Arduino program
1 void setup() {
2 // put your setup code here, to run once:
3 }
initializes configurations
  sets pin modes
  starts serial communications
only execute once

## Slide 5: 2.1 First Arduino program
5 void loop() {
6 // put your main code here, to run repeatedly:
7 }
called immediately after setup()
runs repeatedly

## Slide 6: 2.1 First Arduino program
const int ledPin = 13;
2
3 void setup() {
4 pinMode(ledPin, OUTPUT);
5 }
6
7 void loop() {
8 digitalWrite(ledPin, HIGH);
9 }
1_LightUpLED.ino

## Slide 7: 2.1 First Arduino program
1 const int ledPin = 13;
declare constant integer value ledPin
assign 13 to ledPin

## Slide 8: 2.1 First Arduino program
4 pinMode(ledPin, OUTPUT);
set ledPin to OUTPUT mode
1_LightUpLED.ino

## Slide 9: 2.1 First Arduino program
pinMode(pin, mode);
pin: int, the pin number you want to configure
mode: the mode of operation of the pin.
  INPUT: set the pin to input mode
  OUTPUT: set the pin to output mode
returns: void
Syntax:

## Slide 10: 2.1 First Arduino program
8 digitalWrite(ledPin, HIGH);
send 5V (or 3.3V on 3.3V board) to ledPin

## Slide 11: 2.1 First Arduino program
pin: int, the pin number you want to write the value
mode: the mode of operation of the pin.
  HIGH: set the pin to high voltage level
  LOW: set the pin to low voltage level
returns: void
Syntax:
digitalWrite(pin, mode);

## Slide 12: Contents
2. First Arduino Program
  2.1 Arduino sketch structure
  2.2 Uploading
  2.3 Using delay — a blinking LED
  2.4 Debugging with Serial
  2.5 Summary

## Slide 13: 2.2 Uploading
select correct board
click verify
click upload

## Slide 14: Contents
2. First Arduino Program
  2.1 Arduino sketch structure
  2.2 Uploading
  2.3 Using delay — a blinking LED
  2.4 Debugging with Serial
  2.5 Summary

## Slide 15: 2.3 Using delay — a blinking LED
1 const int ledPin = 13;
2
3 void setup() {
4 pinMode(ledPin, OUTPUT);
5 }
6
7 void loop() {
8 digitalWrite(ledPin, HIGH);
9 delay(1000);
10
11 digitalWrite(ledPin, LOW);
12 delay(1000);
}
2_BlinkLED.ino

## Slide 16: 2.3 Using delay — a blinking LED
9 delay(1000);
pauses the program for a specific amount of time
in milliseconds

## Slide 17: 2.3 Using delay — a blinking LED
delay(milliseconds);
milliseconds: int, time (in milliseconds) to pause
  1000 milliseconds = 1 second
returns: void
Syntax:

## Slide 18: Contents
2. First Arduino Program
  2.1 Arduino sketch structure
  2.2 Uploading
  2.3 Using delay — a blinking LED
  2.4 Debugging with Serial
  2.5 Summary

## Slide 19: 2.4 Debugging with Serial
Serial Monitor can display real-time textual data from Arduino board
is a good way to output
  variables
  parameters
  states

## Slide 20: 2.4 Debugging with Serial
1 const int ledPin = 13;
2
3 void setup() {
4 pinMode(ledPin, OUTPUT);
5 Serial.begin(9600);
6 Serial.print(“Starting LED Blink on pin ”);
7 Serial.println(ledPin);
8 }
3_SerialPrint_BlinkLED.ino — setup()

## Slide 21: 2.4 Debugging with Serial
5 Serial.begin(9600);
start serial communication between the Arduino board and the computer
sets the data rate in bits per second

## Slide 22: 2.4 Debugging with Serial
Serial.begin(speed);
speed: int, it refers to baud rate and defines how quickly data is sent and received between devices.
  the common value is 9600
  115200 for large amounts of sensor data
  more options can be found in Serial Monitor after the board is connected
returns: void
Syntax:

## Slide 23: 2.4 Debugging with Serial
6 Serial.print(“Starting LED Blink on pin ”);
7 Serial.println(ledPin);
send data to the Serial Monitor via serial

## Slide 24: 2.4 Debugging with Serial
Serial.print(value)
Serial.println(value)
value: can be any type of data
  int
  float
  long
  char
  …
Serial.println() adds “\n” at the end
  next printed data will appear on a new line
Syntax:

## Slide 25: 2.4 Debugging with Serial
10 void loop() {
11 digitalWrite(ledPin, HIGH);
12 Serial.println(“LED is ON”);
13 delay(1000);
14
15 digitalWrite(ledPin, LOW);
16 Serial.println(“LED is OFF”);
17 delay(1000);
18 }
3_SerialPrint_BlinkLED.ino — loop()

## Slide 26: Contents
2. First Arduino Program
  2.1 Arduino sketch structure
  2.2 Uploading
  2.3 Using delay — a blinking LED
  2.4 Debugging with Serial
  2.5 Summary

## Slide 27: 2.5 Summary
pinMode(pin, mode)
digitalWrite(pin, value)
delay(milliseconds)
Serial.begin(speed)
Serial.print(value)
Serial.println(value)
digital I/O
time
communication

## Slide 28: 2.5 Summary
how to structure an Arduino script?

## Slide 29: 2.5 Summary
constant declarations
variable declarations
how to structure an Arduino sketch?
e.g. pins

## Slide 30: 2.5 Summary
constant declarations
variable declarations
void setup() {
initializations
}
how to structure an Arduino sketch?
e.g. pins
e.g. pin mode, serial

## Slide 31: 2.5 Summary
constant declarations
variable declarations
void setup() {
initializations
}
void loop() {
main logics
}
how to structure an Arduino sketch?
e.g. pins
e.g. pin mode, serial

## Slide 32: K-12 Microelectronic Workshop Arduino Programming
1 Serial.println(“Thank you!”);