## Slide 1: K-12 Microelectronic Workshop Arduino Programming
1 struct instructor {
2 String name = “Yi Liu”;
3 String department = “Mechanical Engineering”;
4 String university = “University of Vermont”;
5 }

## Slide 2: Contents
4. Sensors
  4.1 HC-SR04 ultrasonic sensor
  4.2 DHT22 temperature and humidity sensor
  4.3 Summary

## Slide 3: 4.1 HC-SR04 ultrasonic sensor

## Slide 4: 4.1 HC-SR04 ultrasonic sensor
Transmitter

## Slide 5: 4.1 HC-SR04 ultrasonic sensor
Receiver
Transmitter

## Slide 6: 4.1 HC-SR04 ultrasonic sensor
Pins
Receiver
Transmitter

## Slide 7: 4.1 HC-SR04 ultrasonic sensor
measure distance by utilizing ultra-sonic waves
T
R
distance
obstacle
HC-SR04

## Slide 8: 4.1 HC-SR04 ultrasonic sensor
measure distance by utilizing ultra-sonic waves
  transmitter emits ultrasonic sounds, and the echo pin is automatically pulled to HIGH
T
R
distance
obstacle
HC-SR04

## Slide 9: 4.1 HC-SR04 ultrasonic sensor
measure distance by utilizing ultra-sonic waves
  transmitter emits ultrasonic sounds, and the echo pin is automatically pulled HIGH
  sound waves bounce back if it hits an obstacle
T
R
distance
obstacle
HC-SR04

## Slide 10: 4.1 HC-SR04 ultrasonic sensor
measure distance by utilizing ultra-sonic waves
  transmitter emits ultrasonic sounds, and the echo pin is automatically pulled HIGH
  sound waves bounce back if it hits an obstacle
  receiver receives the reflected sound, and the echo pin is automatically pulled LOW
  measure the duration of echo pin stays HIGH
T
R
distance
obstacle
HC-SR04

## Slide 11: 4.1 HC-SR04 ultrasonic sensor
measure distance by utilizing ultra-sonic waves
  transmitter emits ultrasonic sounds, and the echo pin is automatically pulled HIGH
  sound waves bounce back if it hits an obstacle
  receiver receives the reflected sound, and the echo pin is automatically pulled LOW
  measure the duration of echo pin stays HIGH
T
R
distance
obstacle
HC-SR04

## Slide 12: 4.1 HC-SR04 ultrasonic sensor
1 const int trigPin = 12;
2 const int echoPin = 13;
3
4 long duration;
5 long distance;
6
7 void setup() {
8 pinMode(trigPin, OUTPUT);
9 pinMode(echoPin, INPUT);
10 Serial.begin(9600);
11 }
7_UltrasonicSensor.ino — setup()

## Slide 13: 4.1 HC-SR04 ultrasonic sensor
13 void loop() {
14 digitalWrite(trigPin, HIGH);
15 delayMicroseconds(10);
16 digitalWrite(trigPin, LOW);
17
18 duration = pulseIn(echoPin, HIGH);
19 distanceCm = duration * 0.034 / 2;
20
21 Serial.print(“Distance: ”);
22 Serial.print(distanceCm);
23 Serial.println(“cm”);
24
25 delay(100);
26 }
7_UltrasonicSensor.ino — loop()

## Slide 14: 4.1 HC-SR04 ultrasonic sensor
5V
Pin 12
GND
Pin 13
Vcc
Trig
Echo
GND

## Slide 15: 4.1 HC-SR04 ultrasonic sensor
15 delayMicroseconds(10);
delay 10 microseconds to ensures the trigger pin stays HIGH for required time to trigger the transmitter

## Slide 16: 4.1 HC-SR04 ultrasonic sensor
delayMicroseconds(microseconds);
microseconds: int, time (in microseconds) to pause
  1000 microseconds = 1 milliseconds
returns: void
Syntax:

## Slide 17: 4.1 HC-SR04 ultrasonic sensor
20 duration = pulseIn(echoPin, HIGH);
measure how long the echoPin stays HIGH

## Slide 18: 4.1 HC-SR04 ultrasonic sensor
20 duration = pulseIn(echoPin, HIGH);
measure how long the echoPin stays HIGH
recall the workflow:
echoPin state
time
HIGH
LOW

## Slide 19: 4.1 HC-SR04 ultrasonic sensor
20 duration = pulseIn(echoPin, HIGH);
measure how long the echoPin stays HIGH
recall the workflow:
  transmitter emits sound wave, and echo pin is pulled HIGH
echoPin state
time
HIGH
LOW
pulse sent

## Slide 20: 4.1 HC-SR04 ultrasonic sensor
20 duration = pulseIn(echoPin, HIGH);
measure how long the echoPin stays HIGH
recall the workflow:
  transmitter emits sound wave, and echo pin is pulled HIGH
  sound wave bounced back after hitting an obstacle, and echo pin still stays HIGH
echoPin state
time
HIGH
LOW
pulse sent

## Slide 21: 4.1 HC-SR04 ultrasonic sensor
20 duration = pulseIn(echoPin, HIGH);
measure how long the echoPin stays HIGH
recall the workflow:
  transmitter emits sound wave, and echo pin is pulled HIGH
  sound wave bounced back after hitting an obstacle, and echo pin still stays HIGH
  receiver receives the echo, and echo pin is pulled LOW
echoPin state
HIGH
LOW
pulse sent
echo received
time

## Slide 22: 4.1 HC-SR04 ultrasonic sensor
20 duration = pulseIn(echoPin, HIGH);
measure how long the echoPin stays HIGH
recall the workflow:
  transmitter emits sound wave, and echo pin is pulled HIGH
  sound wave bounced back after hitting an obstacle, and echo pin still stays HIGH
  receiver receives the echo, and echo pin is pulled LOW
  the duration that echo pin stays HIGH is what pulseIn(echoPin, HIGH) measures
echoPin state
HIGH
LOW
pulse sent
echo received
time
duration

## Slide 23: 4.1 HC-SR04 ultrasonic sensor
pulseIn(pin, value);
pin: int, the pin number to read the pulse
value: HIGH or LOW
returns: long, the length of the pulse, or 0 if no pulse
Syntax:

## Slide 24: Contents
4. Sensors
  4.1 HC-SR04 ultrasonic sensor
  4.2 DHT22 temperature and humidity sensor
  4.3 Summary

## Slide 25: 4.2 DHT22 temperature and humidity sensor

## Slide 26: 4.2 DHT22 temperature and humidity sensor
Sensor

## Slide 27: 4.2 DHT22 temperature and humidity sensor
Sensor
Data processing chip

## Slide 28: 4.2 DHT22 temperature and humidity sensor
Sensor
Data processing chip
Pins

## Slide 29: 4.2 DHT22 temperature and humidity sensor
1 #include “DHT.h”
2 const int dhtPin = 13;
3
4 DHT myDHT(dhtPin, DHT22);
5
6 float humidity;
7 float temperature;
8
9 void setup() {
11 Serial.begin(9600);
12 myDHT.begin();
13 }
8_TemperatureAndHumiditySensor.ino — setup()

## Slide 30: 4.2 DHT22 temperature and humidity sensor
14 void loop() {
15 humidity = myDHT.readHumidity();
16 temperature = myDHT.readTemperature();
17
18 Serial.print(“Humidity: ”);
19 Serial.println(humidity);
20 Serial.print(“Temperature: ”);
21 Serial.println(temperature);
22
23 delay(1000);
24 }
8_TemperatureAndHumiditySensor.ino — loop()

## Slide 31: 4.2 DHT22 temperature and humidity sensor
5V
Pin 12
GND
+
OUT
-

## Slide 32: 4.2 DHT22 temperature and humidity sensor
1 #include “DHT.h”
configuration and data fetching process is like HC-SR04 ultrasonic sensor, but more complicated

## Slide 33: 4.2 DHT22 temperature and humidity sensor
1 #include “DHT.h”
configuration and data fetching process is like HC-SR04 ultrasonic sensor, but more complicated
Arduino IDE provides large amount of libraries
  click library management
  type “DHT Sensor Library”
  install all

## Slide 34: 4.2 DHT22 temperature and humidity sensor
4 DHT myDHT(dhtPin, DHT22);
the way to create a variable of class type

## Slide 35: 4.2 DHT22 temperature and humidity sensor
4 DHT myDHT(dhtPin, DHT22);
the way to create a variable of class type
create a DHT sensor object named myDHT
  DHT is a class from “DHT.h”
  myDHT is the name of the class and can be named anything
  dhtPin tells which pin is being used
  DHT22 tells the object device type

## Slide 36: 4.2 DHT22 temperature and humidity sensor
12 myDHT.begin();
initialize the sensor

## Slide 37: 4.2 DHT22 temperature and humidity sensor
15 humidity = myDHT.readHumidity();
16 temperature = myDHT.readTemperature();
the sensor can be easily fetched using these functions from the library

## Slide 38: 4.2 DHT22 temperature and humidity sensor
How do I know how to use this library???

## Slide 39: 4.2 DHT22 temperature and humidity sensor
How do I know how to use this library???
  check GitHub
    README.md
    keywords.txt

## Slide 40: 4.2 DHT22 temperature and humidity sensor
How do I know how to use this library???
  check GitHub
    README.md
    keywords.txt
  check examples
    files → examples

## Slide 41: Contents
4. Sensors
  4.1 HC-SR04 ultrasonic sensor
  4.2 DHT22 temperature and humidity sensor
  4.3 Summary

## Slide 42: 4.3 Summary
HC-SR04 ultrasonic sensor

## Slide 43: 4.3 Summary
HC-SR04 ultrasonic sensor
  components
    transmitter
    receiver

## Slide 44: 4.3 Summary
HC-SR04 ultrasonic sensor
  components
    transmitter
    receiver
  operating principle
    transmitter sends pulse
    receiver receives echo
    calculate duration

## Slide 45: 4.3 Summary
DHT22 temperature and humidity sensor

## Slide 46: 4.3 Summary
DHT22 temperature and humidity sensor
  components
    humidity resistor
    thermistor
    data processing chip

## Slide 47: 4.3 Summary
DHT22 temperature and humidity sensor
  components
    humidity resistor
    thermistor
  operating principle
    humidity changes resistance of humidity resistor
    temperature changes resistance of thermistor
    chip convert changes into digital signals

## Slide 48: 4.3 Summary
delayMicroseconds(microseconds)
time
advanced I/O
DHT myDHT(pin, type)
myDHT.begin();
myDHT.readHumidity();
myDHT.readTemperature();
pulseIn(pin, value)
DHT22 “DHT.h”

## Slide 49: K-12 Microelectronic Workshop Arduino Programming
1 Serial.println(“Thank you!”);